## Slide 1: Side-Channel Attacks Cyber In Occitanie

## Slide 2: Who am I?
2018
Master in computer science
2021
Thesis in Deep Learning for SCA
From 2021-…
Security evaluator

## Slide 3: Agenda
Context
Side-channel attacks
Demonstration
Statistical distinguishers

## Slide 4: Context

## Slide 5: Context
Company
Develops
Examples
Available on the
market
Critical devices

## Slide 6: Context
Company
Develops
Examples
Available on the
market
Follows regulations
Today

## Slide 7: Context
Common Criteria for Information Technology Security Evaluation (or CC*)
  International standard (ISO/IEC 15408) for computer security certification
  Framework which helps developer for defining
    The Target of Evaluation (TOE)
    The security assets to protect (e.g. secret keys)
    The secure functions related to the TOE (e.g. secure communication, authentication process)
    The level of security assurance (EAL, Evaluation Assurance Level)
  Different security levels
    EAL 1: This is the most basic level, focusing on functional testing to ensure the product performs as specified.
    EAL 2: This level involves more in-depth testing, including structural analysis of the product's components.
    EAL 3: It adds a methodical approach to testing and checking the product's security features.
    EAL 4: This level requires a more rigorous design process, along with thorough testing and review of the product's security.
    EAL 5: It introduces semi-formal methods for design and testing, increasing the level of assurance.
    EAL 6: This level builds upon EAL5 with more formal verification techniques.
    EAL 7: It is the highest level of assurance, requiring formal verification of the product's design and security features.
Functional testing and
structural verifications
+ security testing
(software attacks)
+ physical attacks
+ formal verifications
Who is responsible for making the evaluation process?
*https://www.commoncriteriaportal.org/index.cfm

## Slide 8: Evaluation process
    Weaknesses: physical/logical attacks
    Criticity level for each weakness
    Security assets
    Threats
    Security function
    Hypothesis
    Evaluation Security Level
Company
Thales ITSEF
Security target
Analysis
    Documentary analysis
    Cryptographic analysis
    Audit code
Identification
    Test plan
    Exploitation of one or most weaknesses
    Verdict
Exploitation
ANSSI
Evaluation
Certifies

## Slide 9: Physical attacks

## Slide 10: Physical attacks
Evaluates
Thales ITSEF
Invasive attacks
Semi-Invasive attacks
Non-Invasive attacks
Reverse ingineering /
FIB probing routing
Temporarily / Permanently perturbations
(fault attacks)
Side-channel attacks
Today

## Slide 11: Side-channel Attacks

## Slide 12: Side-channel attacks
Surveillance and Exploitation of an INVOLUNTARY leak from the system
  Related to the communication protocol
  Related to the implementation
  Related to the underlying hardware and physics
Common channels (not exhaustive)
  Errors returned [SW]
  Computation time (duration, cache access time, etc.) [SW]
  Instantaneous current consumption (transistor switching) [HW]
    1 -> 1 or 0 -> 0 consumes less than 1 -> 0 or 0 -> 1
  Electromagnetic radiation [HW]
  Photon emissions, temperature, noise, etc. [HW]
Objective
  Allows attacks on cryptographic algorithms (RSA, ECC, AES, DES, HASH...) to retrieve secret information (key, message)
  Allows attacks on AI embedded systems to retrieve NN architecture, weight value.
  Also helps to understand how the code works (reverse engineering)

## Slide 13: Side-channel attacks
Historical example: Hagelin cipher machine
  Context
    In 1956, Egyptian embassy used Hagelin cipher machine to protect communications.
  Weakness
    The Hagelin machine used 7 wheels (or rotors), which were part of its cryptographic mechanism.
    These wheels needed proper positioning to ensure the encryption and decryption were accurate.
    The Hagelin machine required periodic resetting or reinitialization of their settings, including the positions of the wheels.
  Strategy (MI5)
    Peter Wright (MI5, Scientific expert and counterintelligence officer) proposes installing a microphone in the encryption room.
  Acoustic channel
    Acoustic cryptanalysis is a known technique where sounds produced by mechanical operations can reveal information about the machine's state.
    The noise emitted during the initialization allowed MI5 to determine the position of the wheels during encryption process.
  Result
    MI5 was be able to decrypt the secure communication of the Egyptian embassy.

## Slide 14: Side-channel attacks
Short exercise: 3 switches, 3 light bulbs in another room
  Only one visit is possible
  Which switch turns on each light bulb?
1
2
3
A
B
C

## Slide 15: Side-channel attacks
Short exercise: 3 switches, 3 light bulbs in another room
  Only one visit is possible
  Which switch turns on each light bulb?
1
2
3
A
B
C
ON 5min then OFF
ON
OFF

## Slide 16: Side-channel attacks
Scenario of this talk
  Target of Evaluation: Embedded system
  Security function: Password verification
  Security asset: Password
  Attack: side-channel attack
Password verification process

## Slide 17: Side-channel attacks
Password verification process
Hypotheses
  No limit on the number of attempts
  is stored in memory
  Is brute-force possible?
Can we use side-channel attacks?

## Slide 18: Side-channel attacks
Password verification process
“Divide-and-conquer” strategy
  is validated byte per byte
  Timing difference between the number of correctly verified bytes
In practice
  Assuming operation takes
  Number of requests = instead of (brute-force)
Countermeasure?

## Slide 19: Side-channel attacks
Password verification process
Countermeasure?
  Developing an algorithm which is not time-dependent

## Slide 20: Side-channel attacks
Password verification process
Hypothesis
  No limit on the number of attempts
  is stored in memory
  Is brute-force possible?
Can we use side-channel attacks?

## Slide 21: Side-channel attacks
Scenario of this talk
  Target of Evaluation: Embedded system
  Security function: Password verification
  Security asset: Password
  Attack: side-channel attack

## Slide 22: Side-channel attacks
The CPUs are here 
Capture physical emanation
  Source: Electromagnetic signal
  Equipment: EM probe, oscilloscope, PC
Step 1
  Physical identification

## Slide 23: Side-channel attacks
Capture physical emanation
  Source: Electromagnetic signal
  Equipment: EM probe, oscilloscope, PC
Step 2
  Setup preparation

## Slide 24: Side-channel attacks
Capture physical emanation
  Source: Electromagnetic signal
  Equipment: EM probe, oscilloscope, PC
Step 3
  Signal acquisition

## Slide 25: Side-channel attacks
Leakage model
  A leakage model is a function which characterizes a dependency between a pair and the electromagnetic signal
Attacker’s goal
  Retrieving the dependency between and in a minimum amount of physical traces.
How can we identify such dependencies?

## Slide 26: Side-channel attacks
Step 4: Signal analysis
  A signal characterizes the process conducted by the password verification
5
Next step?
  Which part of the signal is interesting for our study?
  Should we consider all the time samples?
  Do we need to restrict ourselves to a sub-portion of the signal?

## Slide 27: Side-channel attacks
Issues
  Lots of points in a physical signal are not dependent on the sensitive data.
  How can you identify them?
Step 5: Points of interest detection
 Allows the variability identification of on the signal
Other metrics can be used [BDHP21]
[BDHP21] It Started with Templates: The Future of Profiling in Side-Channel Analysis. Batina, L., et al. (2021). In: Avoine, G., Hernandez-Castro, J. (eds) Security of Ubiquitous Computing Systems.

## Slide 28: Side-channel attacks
Issues
  Lots of points in a physical signal are not dependent on the sensitive data.
  How can you identify them?
Step 5: Points of interest detection
No depency with
Dependencies with
Next step?
  How can we exploit these points of interest (POIs)?

## Slide 29: Statistical distinguishers

## Slide 30: Statistical distinguishers
Optimal attack: Maximum likelihood [HRG14]
  Goal: retrieving information on
  Let denotes
[HRG14] Good Is Not Good Enough – Deriving Optimal Distinguishers from Communication Theory. Heuser, A., et al. CHES 2014.
classes

## Slide 31: Statistical distinguishers
Optimal attack: Maximum likelihood [HRG14]
  Goal: retrieving information on
  Let denotes
[HRG14] Good Is Not Good Enough – Deriving Optimal Distinguishers from Communication Theory. Heuser, A., et al. CHES 2014.
How can we estimate ?
  Success Rate: Probability to succeed an attack within attack traces

## Slide 32: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Existing solutions
Generative model
Discriminative model

## Slide 33: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative approach
  Estimation of to then deduce (Bayes’ theorem)
  Historical side-channel attacks [CRR03, SLP05]
Discriminative approach
  Estimation of via the approximation of a decision boundary
  Approach using AI [MPP16, CDP17, MDP20]
[CRR03] Template attacks. Chari, S. et al. CHES 2003.
[SLP05] A stochastic model for differential side channel cryptanalysis. Schindler, W. et al. CHES 2005.
[MPP16] Breaking cryptographic implementations using deep learning techniques. Maghrebi, H. et al. SPACE 2016.
[CDP17] Convolutional neural networks with data augmentation against jitter-based countermeasures - profiling attacks without pre-processing. Cagli, E. et al. CHES 2017.
[MDP20] A comprehensive study of deep learning for side-channel analysis. Masure, L. et al. TCHES 2020.

## Slide 34: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative approach
  Given a trace to which it must associate a sensitive variable , the generative methods approximate the conditional probability
Hypothesis
Template attack [CRR03]
Stochastic attack [SLP05]
[CRR03] Template attacks. Chari, S. et al. CHES 2003.
[SLP05] A stochastic model for differential side channel cryptanalysis. Schindler, W. et al. CHES 2005.

## Slide 35: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative approach
  Given a trace to which it must associate a sensitive variable , the generative methods approximate the conditional probability
Toy example
  Goal: Approximating
  Hypothesis:
1

## Slide 36: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative approach
  Given a trace to which it must associate a sensitive variable , the generative methods approximate the conditional probability
1

## Slide 37: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative approach
  Given a trace to which it must associate a sensitive variable , the generative methods approximate the conditional probability
Steps
Acquire a set of traces such that is unknown
For each trace , we calculate and
We compute the Maximum likelihood:

## Slide 38: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative approach
  Given a trace to which it must associate a sensitive variable , the generative methods approximate the conditional probability
Benefits
Limitations
Information on the exploitated POIs
Confident in the modeling of
Multiple POIs can be exploited simultaneously
Strong hypothesis on the leakage model (Gaussian hypothesis)
The success of attack performances depends on the POIs selection
How can we automate the process?

## Slide 39: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Generative
Discriminative
Bayes’ theorem
Uniformly distributed
Constant
  Maximum likelihood

## Slide 40: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Existing solutions
Generative model
Discriminative model

## Slide 41: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Discriminative approach
  Given a trace to which it must associate a sensitive variable , the discriminative methods approximate the conditional probability
Training process
  Use of loss function to minimize with gradient descent (e.g. Negative Log-Likelihood)
  Not detailed in this talk (see [MDP20])
[MDP20] A comprehensive study of deep learning for side-channel analysis. Masure, L. et al. TCHES 2020.

## Slide 42: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Discriminative approach
  Given a trace to which it must associate a sensitive variable , the discriminative methods approximate the conditional probability
1
Toy example
  Goal: Approximating
  Hypothesis:

## Slide 43: Statistical distinguishers
1
such that

## Slide 44: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Discriminative approach
  Given a trace to which it must associate a sensitive variable , the discriminative methods approximate the conditional probability
1

## Slide 45: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Discriminative approach
  Given a trace to which it must associate a sensitive variable , the discriminative methods approximate the conditional probability
Steps
Acquire a set of traces such that is unknown
For each trace , we calculate and
We compute the Maximum likelihood:

## Slide 46: Statistical distinguishers
Estimation of
  Problem: is unknown and device-dependent
Discriminative approach
  Given a trace to which it must associate a sensitive variable , the generative methods approximate the conditional probability
Benefits
Limitations
No hypothesis on the leakage model
All the tasks (e.g. POIs selection) are automatized
Multiple POIs can be exploited simultaneously
Neural networks can be seen as black-box tools
Construction of adequate statistical model

## Slide 47: Statistical distinguishers
Generative
Discriminative
1
1
Performance
All the tasks (e.g. POIs selection) are automatized
Strong hypothesis on the leakage model (Gaussian hypothesis)
The success of attack performances depends on the POIs selection
Interpretability & Explainability
Confident in the modeling of
Neural networks can be seen as black-box tools
Construction of adequate statistical model

## Slide 48: Countermeasures

## Slide 49: Countermeasures
Desynchronization

## Slide 50: Countermeasures
Desynchronization
Query 1
Query 2
Query 3

## Slide 51: Countermeasures
Masking
  Decomposition of a sensitive variable into such that , , , and
Example
  is a -byte random vector such that and
  is refresh for each query
2 side-channel attacks are required
Estimation of
Estimation of

## Slide 52: Personal recommendations
Online courses
  Amir Moradi’s course: https://www.youtube.com/@AmirMoradi_impsec/playlists
Books
  Embedded Cryptography 1 | Wiley
  Embedded Cryptography 2 | Wiley
  Embedded Cryptography 3 | Wiley
Public datasets:
  ASCAD, AES_HD, AES_RD, DPA contest, …
Open source Librairies:
  For side-channel attacks: SCALib – the Side-Channel Analysis Library: https://scalib.readthedocs.io/
  For deep learning: AISyLab’s framework - GitHub - AISY_Framework: Deep Learning-based Framework for Side-Channel Analysis
International conferences
  CHES, Cascade, Crypto, Eurocrypt, Asiacrypt, …
Side-channel attacks
Online courses
  Andrew NG’s course (Coursera): Machine Learning by Stanford University | Coursera, Deep Learning by deeplearning.ai | Coursera
Books
  Shai Shalev-Shwartz and Shai Ben-David. Understanding Machine Learning: From Theory to Algorithms.
  Christopher M. Bishop and Hugh Bishop. Deep Learning: Foundations and Concepts.
Open source Librairies:
  Tensorflow, PyTorch
International conferences
  NeurIPS, ICML, ECML-PKDD, CVPR, …
Machine-Learning

## Slide 53: Demonstration

## Slide 54: Physical Attacks against Neural Networks Benefits from an adversary’s viewpoint

## Slide 55: Evasion attack
Could be difficult to consider in practice
  White-box scenario: knowledge of the IA architecture, weights, activation functions, etc…
  Black-box scenario: partial knowledge on the AI system (e.g., logits)
Practical issue: How can we generate adversarial examples without any knowledge on the device?
It’s a 7 !
It’s a 3 !
Adversarial examples, KESAKO ?
Notes: Introduire les notions « logits »…

## Slide 56: Evasion attack
It’s a 3 !
Practical issue: How can we generate adversarial examples without any knowledge on the device?
Our idea :
  1) Extraction of the logits through the use of side-channel attacks
  2) Use the state-of-the art adversarial attacks (e.g. ZOO*)
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
It’s a 7 !

## Slide 57: Evasion attack
  Device: ARM Cortex-M7 MCU on a STM32F767 board (216 MHz)
  Embedded AI: a 8-bit quantized denseNET (weights, activations, inputs) with NNOM* tool
  Classification problem: 10 classes (MNIST)
  Channel: Electromagnetic signal (EMV-Technik RF-U 2,5 probe)
* GitHub - majianjia/nnom: A higher-level Neural Network library for microcontrollers.

## Slide 58: Evasion attack
It’s a 0
It’s a 1
It’s a 2
It’s a 3
It’s a 4
It’s a 5
It’s a 6
It’s a 7
It’s a 8
It’s a 9
Softmax
Neural network
Probability
Logits

## Slide 59: Evasion attack
  Targeted function: Softmax function
C code related to the softmax function
vec_in

## Slide 60: Evasion attack
  Targeted function: Softmax function
C code related to the softmax function
Assembly code

## Slide 61: Evasion attack
  Side-Channel attacks
Notes: Corrèle le code de la fonction avec le rayonnement électromagnétique
Comme pour la crypto

## Slide 62: Evasion attack
  Experimental results
    Profiled attack
    Black-box scenario (the attacker has no knowledge on the targeted AI)
  Template
  Logistic regression
Deep learning
Logits
We successfully extract all the logits within 5 traces

## Slide 63: Evasion attack
  Practical issue: How can we generate adversarial examples without any knowledge on the device?
  Our idea :
  1) Extraction of the logits through the use of side-channel attacks
  2) Use the state-of-the art adversarial attacks (e.g. ZOO*)
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
It’s a 7 !
x3
Logits

## Slide 64: Evasion attack
  Generate an adversarial example
    Application of the Zeroth Order Optimization* (ZOO) method
  Recap (ZOO)
  Let be an image and a wrong targeted class that an attacker wants to predict , she looks for an adversarial example such that the following relation is satisfied:
  with
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
Original image
Adversarial example

## Slide 65: Evasion attack
  Practical issue: How can we generate adversarial examples without any knowledge on the device?
  Our idea :
  1) Extraction of the logits through the use of side-channel attacks
  2) Use the state-of-the art adversarial attacks (e.g. ZOO*)
* ‘‘ZOO: Zeroth Order Optimization Based Black-box Attacks to Deep Neural Networks without Training Substitute Models’’, Chen et al., AISec '17
It’s a 3 !

## Slide 66: Thank you Contact: gabriel.zaid@thalesgroup.com